Configuring SPNEGO based SSO with Tomcat and Active Directory

# Introduction
Tomcat provides a low level http request interception mode much more general than servlet filters : valves. Such objects allows one to work on a http request before it reaches the servlet container. To enable automatic authentication, jaaslounge provides you a Valve that realizes the same job than jCifs-ext Authentication Filter, but at a more general level. With this valve, you can use the declarative security, at the application deployment descriptor level.
However, simply using a valve do not allows you to check for roles. This is why we provide a custom realm, which works with Active Directory to obtain groups information associated with the user authenticated by the valve.
# Compilation
The SPNEGO based Valve and Realm provided consists in several classes. To compile these classes you need the following libraries :
- jCifs-ext : version 0.9.4
- jCifs : version 1.1.11 , later versions must not be used as jCifs-ext does not work with.
- catalina.jar : found in directory “server/lib” of tomcat installation
- servlet-api.jar : found in directory “common/lib” of tomcat installation
- commons-logging-api.jar : found in directory “bin” of tomcat installation
# Installation and Configuration
## General
First of all, ensure that your active directory is properly configured. Steps required to configure Active Directory are detailed in the document “AD_Spnego_Configuration”.
Once you have generated a jar containing all the required classes (the package org.jaaslounge.sso.tomcat), copy it to the “server/lib” directory of your Tomcat installation. You then need to configure Tomcat.
## Writing Kerberos configuration
To make use of Kerberos, you need to write an configuration file. This file specifies settings like the Kerberos Realm, address of the server... Here is a sample of such a file, considering that our realm is named MY.DOMAIN.COM, and that our Active Directory server is named adserver.my.domain.com :
[libdefaults]
default_realm = MY.DOMAIN.COM
default_tkt_enctypes = rc4-hmac des-cbc-md5 des-cbc-crc des3-cbc-sha1
default_tgs_enctypes = rc4-hmac des-cbc-md5 des-cbc-crc des3-cbc-sha1

[realms]
 MY.DOMAIN.COM = {
  kdc = adserver.my.domain.com:88
  admin_server = adserver.my.domain.com
  default_domain = MY.DOMAIN.COM
 }

[domain_realm]
 .my.domain.com = MY.DOMAIN.COM
 MY.DOMAIN.COM = MY.DOMAIN.COM

Either save this file as C:\winnt\krb5.ini (on windows), or add an option in CATALINA_OPTS environment variable to point to krb5 configuration file; add the following entry to CATALINA_OPTS : -Djava.security.krb5.conf=path , where “path” points to your Kerberos configuration file.
## Configuring a JAAS Login Module for Kerberos Authentication
By default, jCifs-ext comes with 2 pre-configured aliases to sun's Kerberos Login Modules : jcifs.spnego.initiate and jcifs.spnego.accept. There is no need to change these settings except when you use a Kerberos Login module different from sun's one. You can then specify the path to the login configuration by modifying the CATALINA_OPTS environment variable; add the following entry : -Djava.security.auth.login.config=path, where “path” points to your login configuration file.
## Configuring SpnegoRealm in Tomcat
Open the file server.xml located in the directory “conf” of tomcat installation. Under the section “Engine”, add a “Realm” entry. Suppose that we work with an Active Directory server which dns is adserver.my.domain.com; and the active directory domain is MY.DOMAIN.COM. Then you will add the following lines in your configuration file :
<Realm className="org.jaaslounge.sso.tomcat.spnego.SpnegoRealm"
domainController="adserver.my.domain.com"
servicePrincipalName="HTTP/webserver.my.domain.com"
servicePassword="mypassword"
loginModule="jcifs.spnego.accept"
ldapSearchContext="DC=my,DC=domain,DC=com"
contextFactory="com.sun.jndi.ldap.LdapCtxFactory"
stripGroupNames="true"
/>

The available options for SpnegoRealm are :
- domainController : address of the domain controller.
- servicePrincipalName : principal name identifying the service to allow tomcat to connect to active directory using Kerberos.
- servicePassword : password to be used with the principal name to allow tomcat to connect to active directory using Kerberos.
- loginModule : alias identifying the login module to use to connect to active directory using Kerberos (usually : jcifs.spnego.accept).
- ldapSearchContext : base distinguished name identifying the root context for ldap to search for groups and users.
- contextFactory : fully qualified name of factory class allowing to create the jndi initial context used for ldap search (usually : com.sun.jndi.ldap.LdapCtxFactory).
- stripGroupNames : boolean specifying if the groups obtained from Active Directory must be in short form (stripped) or long form (LDAP full name). For example, on the domain MY.DOMAIN.COM, a group placed in the organization unit “groups” and named “mygroup” will have :
  - LDAP full name : CN=mygroup, OU=groups, DC=my, DC=domain, DC=com
  - stripped name : mygroup
## Configuring SpnegoValve in Tomcat
Open the file context.xml located in the directory “conf” of tomcat installation. Under the section “Context”, add a “Valve” entry. Taking in account the same sample as in the previous point, you will add the following lines to the file :
<Valve className="org.jaaslounge.sso.tomcat.spnego.SpnegoValve"
domainController="adserver.my.domain.com"
domainName="MY.DOMAIN.COM"
/>

The available options for SpnegoValve are :
- domainController : address of the domain controller.
- domainName : name of the domain.